## Slide 1: Seafood HACCP Basic Training
Training Number:
Training Location:
Training Date:
AFDO Region:
Instructor:

## Slide 2
1
Slides prepared to support Seafood HACCP Alliance training courses approved by the Association of Food and Drug Officials (AFDO) which ‘require’ the accompanying training manuals:
Hazard Analysis and Critical Control Point Training Curriculum (SGR 137; Blue Book) 7th edition August 2024
FDA Fish and Fishery Products Hazards and Controls Guidance (Gold Book; SGR 129)
4th edition June 2022

## Slide 3
National Seafood HACCP Alliance for Training and Education
Program Introduction

## Slide 4: Introduction to the Alliance Course and HACCP​
Slide 1
In this chapter, you will learn the:
  Objective of the course
  Format of the course
  Expectations of the participants
  Meaning and importance of HACCP

## Slide 5
Slide 2
Slide 3
Course Objective:
  The FDA HACCP regulation has a training requirement
  for individuals who develop or modify a HACCP plan or review records
  The Alliance training course can be used to demonstrate that you meet this requirement
Course Format:
  HACCP fundamentals using the FDA Hazards Guide
  The FDA seafood HACCP regulation and guidance for developing HACCP Plans
  Practical group exercise to develop a model HACCP Plan

## Slide 6: Audience Role
Slide 4
Participants are encouraged to:
  Ask questions and participate in discussions
  Actively participate in the practical group exercise to develop a HACCP Plan
  Attend all parts of the course

## Slide 7
Slide 5
BLUE
Book
GOLD
Book
The Seafood HACCP Training Manual (blue book) provides:
  •Written content that describes each presentation in the course
  •Reference information and forms to help you develop a HACCP Plan
  The FDA Hazards Guide provides:
    •Guidance for the seafood industry to help them identify hazards for their products and develop effective control strategies
    •A tool for regulatory officials to help them evaluate HACCP Plans for seafood products

## Slide 8: Definitions and Terms
Slide 6
Appendix 4
page 246
Key Definitions and Terms used in the FDA Seafood HACCP regulation and Hazards Guide are provided for reference in Appendix 4

## Slide 9
Slide 7
Slide 8
HACCP stands for Hazard Analysis and Critical Control Points
A HACCP system is
  •Preventive, not reactive
  •A management tool use to protect the food supply
  •Designed to minimize the risk of food safety hazards, but is not zero risk

## Slide 10
Slide 9
Slide 10
National Academy of Sciences Recommendation:
The HACCP approach should be adopted by all regulatory agencies, and it should be mandatory for food processors
Origin of HACCP:
  •Pioneered in the 1960s
  •First used when foods were developed for the space program
  •Adopted by many food processors

## Slide 11: 7 Principles of HACCP
Slide 11
Seven principles of HACCP:
  1) Conduct a hazard analysis
  2) Determine the critical control points (CCPs) in the process
  3) Establish the critical limits
  4) Establish monitoring procedures
  5) Establish corrective actions
  6) Establish verification procedures
  7) Establish record-keeping procedures

## Slide 12: Layers of Controls
Slide 12
HACCP is not a stand-alone system.
HACCP is built on a foundation of Good Manufacturing Practices
HACCP
Sanitation Control Procedures
Good Manufacturing Practices

## Slide 13: Prerequisite Programs and Sanitation Control Procedures
Slide 1
In this chapter you will learn:
  • The importance of prerequisite programs for HACCP
  • Good Manufacturing Practices (GMPs)
  • Sanitation Control Procedures (SCPs)
  • Examples of SCP monitoring

## Slide 14: Prerequisites
Slide 2
Definition:
Prerequisite programs are procedures, including Good Manufacturing Practices (GMPs), that address environmental and operational conditions which provide the foundation for the HACCP system.

## Slide 15
Slide 3
Federal, State, or Local Requirements
  • Food Defense and Biosecurity Requirements
  • Food Safety Modernization Act (FSMA) Requirements
    -Sanitary Transport
    -Food Traceability (some exemptions)
    -Mitigation for intentional adulteration
  • Labeling Requirements
    -Food Allergen Labeling and Consumer Protection Act (FALCPA)
    -Country of Origin Labeling (COOL)
    -Nutritional Labeling and Education Act (NLEA)
  • State and Local Licenses and Permits

## Slide 16
Slide 4
Slide 5
Recommended programs
  •Environmental Monitoring
  •Transportation Controls
  •Recall Programs
  •Supplier controls
  •Preventive maintenance
Required Prerequisite Programs for Seafood HACCP
  •Employee training and training records
  •Current Good Manufacturing Practice (GMPs)
  •Seafood HACCP Regulation-Sanitation Control Procedures

## Slide 17: FSMA addition
Slide 6
Training Requirements - Preventive Controls for Human Food (21 CFR 117)
  •Employees must be qualified to perform assigned jobs
  •Training in food hygiene and food safety
  •Supervisors assure compliance
  •Training records maintained

## Slide 18: Required Training Records
Page 13

## Slide 19: GMP’s 117
Slide 9
Slide 8
  Good manufacturing practices (GMPs) are the basis for determining if process methods produce safe foods and whether products have been processed under sanitary conditions.
Good Manufacturing Practices (21 CFR Part 117 Subpart B)
  •Describes requirements for food processors to ensure safe and sanitary production of foods.
  •First released in 1969 (21 CFR Part 110), GMPs for food manufacturing were revised in 1986 and again in 2015 (21 CFR Part 117).
  •The updated GMPs include prevention of allergen cross-contact.

## Slide 20: GMP’s 117
Slide 10
Appendix 3
page 233
20
  Seafood HACCP programs must be based on a solid foundation in compliance with the GMPs and SCPs.

## Slide 21: Sanitation Control Procedures(SCPs)
Slide 11
  Sanitation control procedures (SCPs) are used by food processing firms to meet requirements in the GMPs.
  SCPs are an effective means to control potential food safety hazards that might be associated with the processing environment and employee practices.

## Slide 22: SSOP’s- Written Procedures
Slide 12
Sanitation Control Procedures:
Recommended:
  •Written Sanitation Standard Operating Procedures (SSOPs).
  Required
  •Monitoring
  •Corrections
  •Recordkeeping

## Slide 23: Example of Sanitation Control Procedures
Slide 13
Examples of Sanitation Control Procedures
Control of bacterial cross contamination hazard
  •Maintain product flow
  •Location of hand washing stations
  •Equipment cleaning and Sanitizing
Control of chemical cross contamination and/or allergen cross-contact hazards
  •Proper chemical storage
  •Proper chemical labeling
  •Correct use of chemicals
  •Production scheduling to prevent allergen cross-contact.

## Slide 24: 8 Key Areas of Sanitation
Slide 14
Eight Key areas of sanitation:
  1)Safety of water
  2)Condition and cleanliness of food contact surfaces
  3)Prevention of cross contamination
  4)Maintenance of hand washing, hand sanitizing and toilet facilities
  5)Protection from adulterants
  6)Labeling, storage and use of toxic compounds
  7)Employee health
  8)Exclusion of pests

## Slide 25
Slide 15
Slide 16
1) Safety of water
  •Source and treatment of water that comes in contact with food or food contact surfaces
  •Water used in the manufacture of ice
  •Cross-connections between potable and non-potable
  water supplies
2) Condition and cleanliness of food contact surfaces
  •Design, workmanship, maintenance, and materials used for food contact surfaces
  •Routine scheduled cleaning and sanitizing of food contact
  surfaces including gloves and outer garments

## Slide 26
Slide 17
Slide 18
3) Prevention of cross-contamination
  •Employee hygiene practices
  •Employee food handling practices
  •Plant design and layout
  •Physical separation of raw and ready-to-eat products
4) Maintenance of hand washing, hand sanitizing, and toilet
facilities:
  •Maintenance and location of hand washing, hand sanitizing, and toilet facilities
  •Maintenance of adequate sewage disposal system

## Slide 27
Slide 19
Slide 20
5) Protection from adulterants
  •Protect food, food contact surfaces, and food packaging material from contaminants.
6) Labeling, storage and use of toxic compounds

## Slide 28
Slide 21
Slide 22
7) Employee health conditions:
  •Controls are necessary to ensure that employee health
  conditions do not cause food contamination.
6) Exclusion of pests:
  • Pests must not be present in the food processing facility.

## Slide 29: SCPs in GMPs 117
Pages 21-22

## Slide 30: Monitoring SCPs
Pages 24-25

## Slide 31: Monitoring SCPs
Slide 24
  Required Elements of SCP Monitoring Records
    •Name and address of the firm
    •Date and time of the recorded activity
    •Include all of the eight key sanitary concerns pertinent to the operation
    •Monitoring procedure and appropriate frequency
    •Monitoring results
    •Corrections taken
    •Signature or initials of person conducting the monitoring

## Slide 32
Slide 25
A facility processes only chilled Atlantic Salmon and Pacific Cod fillets
•Does SCP concerning safety of water apply? How?
  •Does SCP concerning protection from adulterants apply? How?
Page 27

## Slide 33: SCP Requirements
Slide 26
Sanitation in the Seafood HACCP Regulations:
  SCPs are required and written SSOPs are recommended,
  Monitoring for the eight key areas of sanitation is required,
  Recording monitoring results is required,
  Making corrections and documenting them is required.

## Slide 34: HACCP vs. SCP’s
Slide 27
Hazard | Control | Type of Control | Control Program
Histamine | Time and temperature controls for fish | Product specific | HACCP
Pathogen survival | Time and temperature controls for smoking fish | Processing step | HACCP
Contamination with pathogens | Wash hands before touching product | Employee | Sanitation or SCP
Contamination with pathogens | Limit employee movement between raw and cooked areas | Employee | Sanitation or SCP
Contamination with pathogens | Clean and sanitize food contact surfaces | Plant environment | Sanitation or SCP
Chemical contamination | Use only food-grade grease | Plant environment | Sanitation or SCP

## Slide 35
Example SSOP ‘written program’
and accompanying records
Pages 30-39

## Slide 36: Seafood Safety Hazards
Slide 1
In this chapter you will learn:
  • Food Safety Hazards that have been associated with seafood and are considered “reasonably likely to occur” if not subject to appropriate controls

## Slide 37
Slide 2
Hazards: a biological, chemical or physical agent that is reasonably likely to cause illness or injury in the absence of appropriate controls
Undesirable conditions may not impose a particular food safety hazard, but they are subject to other regulatory controls and pre-requisite requirements (i.e., GMPS and Sanitation Control Procedures (SCPs). Examples include:
  Insects
  Hair
  Filth
  Spoilage
  Economic Fraud
  Violations of regulatory food safety standards not directly related to safety

## Slide 38: Categories for Seafood Safety Hazards
Slide 3
Potential seafood safety hazards can be grouped into two categories:
Species-related hazards
Process-related hazards

## Slide 39: Species- and Process-Related Hazards
Slide 4
Process-Related Hazards
  Pathogenic Bacteria Growth and Toxin Formation (Other than Clostridium botulinum) as a Result of Time and Temperature Abuse
  Clostridium botulinum Toxin Formation
  Pathogenic Bacteria Growth and Toxin Formation as a Result of Inadequate Drying
  Staphylococcus aureus Toxin Formation in Hydrated Batter Mixes
  Pathogenic Bacteria Survival Through Cooking or Pasteurization
  Introduction of Pathogenic Bacteria After Pasteurization and Specialized Cooking Processes
  Undeclared Major Food Allergens and Certain Food Intolerance Substances
  Metal and glass inclusion
Species-Related Hazards
  Pathogens from the Harvest Area (molluscan shellfish only)
  Parasites
  Natural Toxins
  Scombrotoxin or Histamine Formation (certain species of finfish only)
  Environmental Chemical Contaminants Including Pesticides Methylmercury
  Aquaculture Drugs (farm raised)

## Slide 40: Pathogens in Seafood
Slide 5
Slide 6
Microorganisms that can be pathogenic and cause seafoodborne illnesses:
  Bacteria
  Viruses
  Protozoa
  Microscopic parasites
Bacterial Hazards:
  Foodborne infection
  Foodborne intoxication

## Slide 41: Pathogen Controls
Slide 7
Control strategies for pathogens in seafood:
  Source controls for high risk products like raw molluscan shellfish require that they only be harvested from waters that do not have elevated levels of pathogens
  Prevent or reduce pathogen growth to an acceptable level by: freezing, refrigeration (minimizing exposure to temperatures above 40°F), drying, acidifying, fermenting, or salting
  Eliminate or kill pathogens by cooking, pasteurizing, or using lethal non-thermal treatments

## Slide 42: Pathogens Growth
Slide 8
Slide 9
What bacteria need for favorable growth:
  Food (nutrients from the seafood)
  Water (moisture in the seafood)
  Proper temperature
  Air, minimal air or no air (reduced-oxygen)

## Slide 43: Primary Microbial Pathogens
Slide 10
Pathogens of Concern for Seafood Products:
Sporeforming bacteria
  Clostridium botulinum
  Bacillus cereus
  Clostridium perfringens
Non-Sporeforming bacteria
  Listeria monocytogenes
  Salmonella spp. (e.g., S. typhimurium, S. enteriditis)
  Shigella spp. (e.g., S. dysenteriae)
  Pathogenic Staphylococcus aureus
  Vibrio spp. (e.g., V. cholerae, V. parahaemolyticus, V. vulnificus)
  Others (Campylobacter jejuni, Yersina enterocolitica, Shigella spp. and Escherichia coli)

## Slide 44: Specific Pathogen Controls
Slide 11
Pathogens of Concern for Seafood Products:
Sporeforming bacteria
  Clostridium botulinum
  Bacillus cereus
  Clostridium perfringens
Non-Sporeforming bacteria
  Listeria monocytogenes
  Salmonella spp. (e.g., S. typhimurium, S. enteriditis)
  Shigella spp. (e.g., S. dysenteriae)
  Pathogenic Staphylococcus aureus
  Vibrio spp. (e.g., V. cholerae, V. parahaemolyticus, V. vulnificus)
  Others (Campylobacter jejuni, Yersina enterocolitica, Shigella spp. and Escherichia coli)

## Slide 45: Specific Pathogen Controls
Slide 12
Some controls for Bacillus cereus in seafood:
  Proper sanitation to prevent product contamination (product source, process facilities and personnel)
  Proper chilling rates for warm prepared food
  Proper refrigeration for prepared, ready-to-eat (RTE) food with extended shelf lives

## Slide 46: Specific Pathogen Controls
Slide 13
Some controls for Listeria monocytogenes in seafood:
  Proper sanitation to prevent product contamination (product source, process facilities, and personnel)
  Proper refrigeration to prevent growth
  Proper cooking
  Prevent cross-contamination after cooking

## Slide 47: Specific Pathogen Controls
Slide 14
Some controls for Salmonella spp. in seafood:
  Proper sanitation to prevent product contamination (product source, process facilities and personnel)
  Proper refrigeration to prevent growth
  Proper cooking
  Prevent cross-contamination after cooking

## Slide 48: Specific Pathogen Controls
Slide 15
Some controls for Staphylococcus aureus in seafood:
  Proper sanitation to prevent product contamination (product source, process facilities and personnel)
  Proper refrigeration to prevent growth
  Proper cooking
  Prevent cross-contamination after cooking

## Slide 49: Specific Pathogen Controls
Slide 16
Some controls for Vibrio cholerae, Vibrio parahaemolyticus and Vibrio vulnificus in seafood:
  Product harvested from approved sources
  Proper refrigeration from harvest through processing
  Proper cooking
  Consumption advisories for more susceptible consumers

## Slide 50: Viruses
Slide 17
Hazards from viruses in foods
  Not truly "alive“
  Exist everywhere
  Do not grow in food
  Do not spoil food
  Transmitted by people, food and contaminated water
  Cause illness by infection

## Slide 51: Viruses
Slide 19
Hazards from viruses in foods
  Not truly "alive“
  Exist everywhere
  Do not grow in food
  Do not spoil food
  Transmitted by people, food and contaminated water
  Cause illness by infection
Slide 18
Viruses:
  Hepatitis A virus causes fever and abdominal discomfort, followed by jaundice
  Norovirus group (formerly Norwalk Virus) causes nausea, vomiting, diarrhea, and abdominal pain (gastroenteritis); headache and low-grade fever may also occur
Some controls for viruses in seafood:
  Product from approved sources
  Thorough cooking

## Slide 52: Parasites
Slide 21
Hazards from viruses in foods
  Not truly "alive“
  Exist everywhere
  Do not grow in food
  Do not spoil food
Slide 20
Parasites are organisms that need a host to survive.
  Thousands of kinds exist worldwide but less than 100 types are known to infect people through food consumption
  Types of concerns for seafood or water:
    Parasitic worms (e.g., roundworms/nematodes, tapeworms/ cestodes, and flukes/trematodes)
Methods of preventing transmission of parasites to foods by fecal contamination include:
  Good personal hygiene practices by food handlers
  Proper disposal of human feces
  Elimination of insufficiently treated sewage to fertilize crops
  Proper sewage treatment

## Slide 53: Parasites
Slide 23
Hazards from viruses in foods
  Not truly "alive“
  Exist everywhere
  Do not grow in food
  Do not spoil food
Slide 22
Parasitic Worms:
  Cryptosporidium parvum
  Nematodes and roundworms (Anasakis simplex, Pseudoterranova dicepiens, Eustrongylides spp. and Gnathostoma spp.)
  Cestodes or tapeworms (Diphyllobothrium latum)
  Trematodes or flukes (Chlonorchis sinensis, Heterophyes spp., Metagonimus spp., and others)
Some controls for Anisakis simplex, P. decipiens and D. latum parasites in seafood:
  Proper freezing
  Proper cooking

## Slide 54: Species-Related Hazards from Harvest/Growing Waters
Slide 24
Species-Related Hazards Associated with the Harvest/Growing Area
  Natural Toxins
  Environmental Chemical Contaminants
  Aquaculture Drugs

## Slide 55: Natural Toxins
Slide 25
Biotoxins – naturally occurring hazards:
  Shellfish Biotoxins- Amnesic Shellfish Poisoning (ASP; domoic acid)
    Diarrhetic Shellfish Poisoning (DSP; okadaic acid)
    Neurotoxic Shellfish Poisoning (NSP)
    Paralytic Shellfish Poisoning (PSP; saxitoxins)
  Ciguatera Fish Poisoning (CFP)
  Tetrodotoxins (puffer fish poisoning)

## Slide 56: Natural Toxins Controls
Slide 26
Slide 27
Control for ciguatera in seafood:
  Do not process certain fish harvested from waters that have been designated as potentially ciguatoxic
Control for shellfish biotoxins in seafood:
  Only harvest approved shellfish products from approved waters

## Slide 57: Natural Toxins Controls
Slide 28
Slide 29
Control for gempyltoxin in seafood:
  Do not process certain potentially gempylotoxic fish
Control for tetrodotoxin in seafood:
  Do not process certain fish (puffer fish) that have been designated as potentially tetrodotoxic

## Slide 58: Environmental Chemical Contaminants
Slide 30
Controls for Environmental Chemical Contaminants (Pollutants)
  Do not harvest or sell fish or shellfish from waters that have been closed by federal, state, or local authorities due to environmental pollution
  Properly locate and monitor aquaculture farming operations to prevent pond contamination from runoff, and previous or new human activities. Testing for chemical contaminants of concern

## Slide 59: Aquaculture Drugs: Illegal or Improper Use
Slide 31
Some controls for use of aquaculture drugs:
  When necessary, only use certain controlled drugs in the manner prescribed by a recognized veterinary expert
  Test for any excessive residuals in final products

## Slide 60: Scombrotoxin(histamine poisoning)
Slide 32
Control for potential scombrotoxin in seafood:
  Temperature controls from the moment of harvest through processing, storage, and product distribution

## Slide 61: Process-Related Hazards
Slide 33
Other Process-Related Food Safety Hazards
  Food Intolerance Substances (FIS)
  Food Allergens
  Metal and Glass Inclusion

## Slide 62: Process-Related Hazards
Slide 34
Slide 35
Controls for intentionally added ingredients in seafood:
  Use proper type and amount of ingredients
  Label product to inform consumers (e.g., sulfites and yellow #5)
Examples of Food and Color Additives
  Preservatives (e.g. nitrite, sulfites)
  Nutritional additives (e.g. vitamins)
  Color Additives (FD&C Yellow No. 5)

## Slide 63: Food Allergens
Slide 36
Slide 37
Control for ciguatera in seafood:
  Do not process certain fish harvested from waters that have been designated as potentially ciguatoxic
Control for shellfish biotoxins in seafood:
  Only harvest approved shellfish products from approved waters

## Slide 64: Process-Related Hazards
Slide 33
Other Process-Related Food Safety Hazards
  Food Intolerance Substances (FIS)
  Food Allergens
  Metal and Glass Inclusion

## Slide 65: Physical Hazards
Example:​ The following are examples of materials that may be physical hazards:​ ​ | 
Material​ | Why a hazard?​
Glass​ | Cuts, bleeding; may require surgery to find or remove​
Metal​ | Cuts, broken teeth; may require surgery to remove​
Slide 38
Physical Hazard:​
Any extraneous matter not normally found in food that could cause physical injury

## Slide 66: Physical Hazards Controls
Slide 39
Slide 40
Controls for potential metal inclusion in seafood: ​
  Monitoring equipment for wear and breakage ​
  Screening products with metal detectors
Control for potential glass inclusion in seafood:
  Examination of glass containers for breakage​

## Slide 67: Preliminary Steps in Developing HACCP Plan
Slide 1
In this chapter you will learn:
  • The importance of preliminary steps in developing the HACCP plan

## Slide 68: Get Ready!
Slide 2
Preliminary steps:​
  • Assemble HACCP team​
  • Describe the product, intended use and consumers​
  • Develop a Process Flow Chart​
  • Develop a Process Description​

## Slide 69: HACCP TEAM…Who is involved?
Managers Sanitation​ Processing​

## Slide 70: Get Ready!
Slide 2
Preliminary steps:​
  • Assemble HACCP team​
  • Describe the product, intended use and consumers​
  • Develop a Process Flow Chart​
  • Develop a Process Description​

## Slide 71: What is involved?
Slide 3
Product Description should include:​
  • Type of seafood product (species and finished product form)​
  • Where product is purchased​
  • How product is received, stored, and shipped​
  • How product is packaged​
  • Intended use

## Slide 72: What is involved?
Useful Product Description Chart​
Page 73

## Slide 73: Processing steps involved?
Page 73
Slide 5

## Slide 74: Introduce XYZ Seafood Company (See pages 74-76)
Page 73
Slide 6

## Slide 75: XYZ Processing Steps
Slide7
Example process flow diagram for production of fresh mahi-mahi fillets for XYZ Seafood Company
Process Flow Chart

## Slide 76: Principle 1: Hazard Analysis
Slide 1
In this chapter you will learn how to:​
  • Conduct a hazard analysis​
  • Identify significant hazards​
  • Identify control measures

## Slide 77: Key Definitions
Slide 2
Definition: A hazard is any biological, chemical or physical agent that is reasonably likely to cause illness or injury in the absence of control(s).
Food Safety Hazards
Biological​
Chemical​
Physical​

## Slide 78: Why conduct a Hazard Analysis?
Slide 3
The hazard analysis is conducted to identify:​
• All potential food safety hazards,​
• Which of these hazards are significant, and​
• Measures to control the significant hazards.​

## Slide 79: How to conduct a Hazard Analysis?
Slide 4
There are five steps in a hazard analysis:​
  1) List process steps​
  2) Identify potential food safety hazards​
  3) Determine if the hazard is significant​
  4) Justify the decision​
  5) Identify control measure(s)
5 Steps​

## Slide 80: Use the Hazard Analysis Worksheet
Slide 5

## Slide 81: STEP 1– Enter Processing Steps​
Slide 6
Step 1: Enter each of the processing steps from the process flow chart in Column 1 of the hazard analysis worksheet. Each step will have its own block on the worksheet and should be listed in the same order as on the process flow chart.
5 Steps​
“Fresh Mahi-mahi Fillets”​
Processing Steps​
Flow Diagram from​
Chapter 4, Page 75​
Chapter 4, Page 75

## Slide 82: List all Processing Steps
Receiving Fresh/Raw Fillets
Refrigerated Storage
Trim
Weigh/ Pack/Label
Finish Product Refrig. Storage
Column 1: List all of the processing steps from the Process Flow Chart

## Slide 83: STEP 2– List Potential Food Safety Hazards
Slide 7
Step 2. List potential food safety hazards. It is important to list every identified hazard at each listed processing step.
5 Steps​
Slide 8
Use the Hazards Guide as a tool to identify potential hazards.​

## Slide 84: Search for the potential hazards for the Fresh ‘Wild’ Mahi-mahi Fillets
Tables 3-2 and 3-3
Species-Related Hazards
Table 3-4
Process-Related Hazards

## Slide 85: One Species-related hazard
Table 3-2

## Slide 86
Notice two hazards in Chapter 19
Table 3-4
Four Process-related hazard

## Slide 87: Hazard Analysis for the XYZ Seafood Company should include 5 potential hazards:
Species-related Hazards
1. Histamine formation (Chapter 7)
Process-related Hazards
Pathogenic bacterial growth-temperature abuse (Chapter 12)
Allergens (Chapter 19)
Food Intolerance Substances (Chapter 19)
Metal inclusion (Chapter 20)
Table 3-2
Table 3-4

## Slide 88: Inclusive Method

## Slide 89: STEPS 3 & 4 – Hazard Evaluation & Justification
Slide 12
Steps 3 and 4: Hazard Evaluation and Justification. Determine​which hazards are significant and explain why.​
5 Steps​
Simply answer the questions in the Hazard Analysis

## Slide 90: Exercise: Complete the Hazard Analysis Worksheet
Simply answer the questions in order for each listed potential hazard at each processing step
FDA Hazards Guide provides some recommendations in the respective hazard chapters

## Slide 91
Slide 13
Slide 14
To determine if a hazard is significant, consider two questions:​
1) Is the hazard reasonably likely to occur in the finished product in the absence of control?​
2) Is the hazard likely to cause consumer illness?
Example – Fresh/Raw Mahi-Mahi ​
  Which Hazards are Significant at the first process step, Receiving? ​
  Histamine (Yes or No?) ​
  Pathogen Growth - Temperature Abuse (Yes or No?) ​
  Allergens (Yes or No?) ​
  Food Intolerance Substances (Yes or No?) ​
  Metal Inclusion (Yes or No?) ​

## Slide 92
Justify your ‘Yes or No’ decisions
see page 93

## Slide 93: BRIEF SUMMARY based on the FDA Guide that provides more recommended details
Column 2 Potential Hazards (Likely to Occur) | Columns 3 & 4 Is the hazard significant in this processing operation | 
Histamine | YES | Mahi is potential scombrotoxic fish species subject to temperature abuse
Pathogen Growth -Temp. Abuse | NO | Mahi intended to be cooked before consumption
Undeclared Food Allergens | YES | Fish are food allergens
Food Intolerance Substances (FIS) | NO | No FIS or food additives used or added in this processing operation
Metal Inclusion | NO | Not likely to occur in processing steps

## Slide 94: STEPS 5 – Identify control Measures (Column 5)
Slide 16
Step 5: Identify Control Measures for each significant hazard.
5 Steps​
Slide 17
Control measures can be used to:​
  • Prevent a food safety hazard,​
  • Eliminate a food safety hazard, or​
  • Reduce a food safety hazard to an acceptable level.​

## Slide 95: Control Measures
Slide 18
Control Measures for Pathogenic Bacteria, Viruses, Parasites​
Bacteria​
  1) Time/temperature controls​
  2) Heating and cooking​
  3) Freezing​
  4) Fermentation and/or pH controls​
  5) Salt or other preservatives​
  6) Drying​
  7) Source controls​
  18) Other processes (e.g. high hydrostatic pressure and irradiation)​
​
Viruses​
  1) Cooking​
  2) Source controls​
​
Parasites​
  1) Cooking​
  2) Freezing​

## Slide 96: Control Measures
Slide 19
Control Measures for Chemical and Physical Hazards Chemical Hazards (Natural toxins, pesticides, drug residues, unapproved food and color additives, histamine
1)Source controls
2)Time/temperature controls
3)Production controls
4)Labeling controls
Physical Hazards (Metal, glass, etc.)
1)Source controls
2)Production controls

## Slide 97: BRIEF SUMMARY based on the FDA Guide that provides more recommended details
Column 2 Potential Hazards (Likely to Occur) | Columns 3 & 4 Is the hazard significant in this processing operation |  | Column 5 Necessary Controls
Histamine | YES | Mahi is potential scombrotoxic fish species subject to temperature abuse | Time and Temperature controls (Chapter 7)
Pathogen Growth -Temp. Abuse | NO | Mahi intended to be cooked before consumption | Chapter 12
Undeclared Food Allergens | YES | Fish are food allergens | Proper product labeling (Chapter 19)
Food Intolerance Substances (FIS) | NO | No FIS or food additives used or added in this processing operation | 
Metal Inclusion | NO | Not likely to occur in processing steps | Chapter 20 (page 386)

## Slide 98: Hazard Analysis Worksheet
Every ‘Yes’ in column 3
requires a response in column 5 and 6
Pages 95-97

## Slide 99: Hazard Analysis Worksheet
Every ‘Yes’ in column 3
requires a response in column 5 and 6
Pages 95-97

## Slide 100: Hazard Analysis Worksheet
Every ‘Yes’ in column 3
requires a response in column 5 and 6
Pages 95-97

## Slide 101: Be sure to identify all potential FOOD SAFETY Hazards
Slide 21
All food safety hazards must be considered in the Hazard Analysis, but it is not necessary to distinguish the hazards as biological, chemical or physical hazards.

## Slide 102
End Chapter 5: Principle 1
Hazard Analysis

## Slide 103: Principle 2: Determine Critical Control Points
Slide 1
In this chapter you will learn:
  •The definition of a Critical Control Point (CCP).
  •The relationship between significant hazards, control measures, and CCPs.
  •How CCPs may be different for different products and processes.
  •Tools to help you determine which steps are CCPs.
  •Examples of CCPs for various food safety hazards.

## Slide 104: What’s a Critical Control Points
Slide 2
Slide 3
Definition: A Critical Control Point is a step at which control can be applied to prevent, eliminate a food safety hazard, or reduce it to an acceptable level.
CCP placement must be at the processing step or steps that adequately control the significant hazard.

## Slide 105: Hazard Prevention
Control Measures Formulation Time/Temp Control Supplier Certificates
CCPs
Mixing Step
Refrigerated Storage Step Receiving Step
Slide 4
CCPs can be steps where hazards can be prevented.

## Slide 106: Hazard Elimination
Control Measures Cooking
Use of Metal Detection Freezing Procedures
CCPs
Cook Step
Metal Detector Step Freeze Step
Slide 5
CCPs can be steps where hazards can be eliminated.

## Slide 107: Hazard Reduction
Control Measure Source Controls Time/Temp Control
CCP
Receiving Step Cook Step
Slide 6
CCPs can be steps where hazards can be reduced to acceptable level.

## Slide 108: More than one …
Slide 7
Multiple Hazards and Single CCP
Product = Live oysters (shellstock)
Hazards = Harvest site pathogens + Natural Toxins + Chemical
Contaminants
Single CCP = Receiving
Single Hazard and Multiple CCPs
Product = Fresh Tuna loins
Hazard = Histamine
Multiple CCPs = Receiving + Refrigerated Storage

## Slide 109: Product & Process Specific …
Slide 8
CCP are product- and process-specific and impacted by:
  •Layout of the plant or processing line,
  •Finished product formulation,
  •Process flow or sequence of processing steps,
  •Processing equipment,
  •Ingredients,
  •Sanitation or other support programs.

## Slide 110
CCP Decision Tree
(optional tool)
Page 103

## Slide 111: Completed Hazard Analysis 105 - 107
Every ‘Yes’ in column 3 requires a response in column 6
CCP
CCP

## Slide 112: Completed Hazard Analysis 105 - 107
CCP
CCP
Every ‘Yes’ in column 3 requires a response in column 6
Completed Hazard Analysis 105 - 107

## Slide 113: Completed Hazard Analysis 105 - 107
CCP
Every ‘Yes’ in column 3 requires a response in column 6
Completed Hazard Analysis 105 - 107
CCP
CCP

## Slide 114: Conclusions from the Hazard Analysis
Histamine is a significant food safety hazard and there are three CCPs for this hazard:
    CCP 1. Receive fresh fish
    CCP 2. Refrigerated storage, and
    CCP 3. Finished product refrigerated storage
Undeclared food allergen is a significant food safety hazard and there is one CCP for this hazard:
  CCP 4. Weigh/Pack/Label

## Slide 115: Remember to use the recommendations in the FDA Guide
For example, ‘Likely CCPs’ for histamine formation (FDA Guide, Chapter 7)
and food allergens
(FDA Guide, Chapter 19)
Tip

## Slide 116: “CCP either here or later”
Tip
Every ‘Yes’ in column 3
requires a response in column 6
Hazard here
CCP later

## Slide 117
End Chapter 6: Principle 2
Determine Critical Control Points
Got it ?

## Slide 118: Principle 3: Establish Critical Limits
Slide 1
In this chapter you will learn:
  •Definition of critical limit.
  •How to determine critical limits for a CCP.
  •The relationship between critical limits and operating limits.
  •Use of the HACCP plan form.

## Slide 119: What’s is a Critical Limit?
Slide 2
Definition:
Critical Limit: A maximum and/or minimum value to which a biological, chemical or physical parameter must be controlled at a CCP to prevent, eliminate or reduce the occurrence of a food safety hazard to an acceptable level.

## Slide 120: Sources & Examples …

## Slide 121: Options and details…
Slide 8
Slide 7
see pages 112-113
Option No. 1
Product: Fish cakes
Hazard — pathogen survival through cooking CCP — fryer
Critical limit — no pathogens detected
Option No. 2
Product: Fish cakes
Hazard — pathogen survival through cooking
CCP — fryer
Critical limit — minimum internal temperature of 165°F for 36 seconds

## Slide 122: Options and details…
Slide 7
see pages 112-113
Option No. 3
Product: Fish cakes
Hazard —pathogen survival
CCP — fryer
Critical limit — minimum fryer oil temperature of 350°F Critical limit — maximum fish cake thickness of ¾ inch Critical limit — minimum cook time in the oil of two minutes

## Slide 123: Using Operating Limits
Slide 10
Definition:
Operating Limits: Criteria that are more stringent than critical limits and that are used by an operator to reduce the risk of a deviation.

## Slide 124
Using ‘Lot’
Designations
Page 115

## Slide 125: Critical Limits should be specified in the written HACCP Plan
Slide 12
Blank HACCP Form

## Slide 126: Optional HACCP Plan Forms (both must contain same information)
Landscape
Portrait

## Slide 127: Expected Information in all HACCP Plans

## Slide 128: Building a HACCP Plan Form for each CCP
Column 1 & 2: List all of the identified CCPs and identified hazards
Hazard Analysis Worksheet
HACCP Plan From

## Slide 129: Recommended Critical Limits
REMINDER: The FDA Guide contains control strategies with recommended CL’s
Processors may select alternative CL’s ‘however’ equivalent effectiveness MUST be demonstrated and documented

## Slide 130: Select a Control Strategy
CONTROL STRATEGY selected from the FDA Guide
CCP – Receiving
Hazard - Histamine
CHP 7

## Slide 131: Proceed through the selected Control Strategies
Note all listed options to suit different situations
When applicable, there can be different strategies for
primary vs. secondary processors
Note the details associated with OR’s and AND’s

## Slide 132: Select the best control to situation and assure effective control for the potential hazard
TRANSIT CONTROL CRITICAL LIMITS
Transit temperature records, or
Completely surrounded by ice on delivery, or
Use of ice; AND internal fish temperature, or
Frozen gel-packs; AND internal fish temperature, or
Transit time (< 4 hours); AND internal fish temperature
Tip
Notice ‘ORs & ANDs ’

## Slide 133: HACCP Plan for XYZ Seafood Company
FDA Guide, Chapter 7

## Slide 134
HACCP Plan for XYZ Seafood Company
Critical Limits based on recommendations in the FDA Hazards Guide

## Slide 135: Want some more ?
End Chapter 7:Principle 3
Establish Critical Limits

## Slide 136: Principle 4: Critical Control Point Monitoring
Slide 1
In this chapter you will learn:
  •Definition of monitoring,
  •Purpose of monitoring,
  •Design of a monitoring system,
  •Methods and equipment for monitoring critical limits.

## Slide 137: What is a Monitoring?
Slide 2
  Definition:
  Monitoring: A planned sequence of observations or measurements to assess whether a CCP is under control and to produce an accurate record to demonstrate that critical limits have been met.
Slide 3
Purpose of Monitoring
  •To ensure that a critical limit is met,
  •To provide documentation that critical limits have been met,
  •To identify when there is loss of control (a deviation occurs at a CCP).

## Slide 138
Slide 4
What ?
How ?
Who ?
When ? (frequency)
Elements of Monitoring
  •What will be monitored?
  •How will monitoring be performed?
  •What is the frequency of monitoring?
  •Who will conduct the monitoring?
4 required parts for proper MONITORING

## Slide 139: What ?
Slide 5
What?
What will be monitored?
A measurement or observation to assess if the CCP is operating within the critical limit.

## Slide 140: How ?
Slide6
How?
How will monitoring be performed?
  •Measurements (quantitative critical limits) or observations (qualitative critical limits).
  •Needs to be real-time and accurate.

## Slide 141: What? (frequency)
Slide 7
When?(frequency)
What is the frequency of monitoring?
  •Monitoring frequency should be sufficient to ensure that the critical limit is met.
  •Monitoring frequency can be non-continuous or continuous.

## Slide 142: What? (frequency)
Slide 8
Who?
Who will monitor?
Person(s) trained to perform the specific monitoring activity and/or a continuous monitoring device.

## Slide 143: Monitoring requires training
Slide 9
Those responsible for monitoring a CCP should
  •Be trained in the CCP monitoring techniques.
  •Fully understand the importance of CCP monitoring.
  •Have ready access to the monitoring activity.
  •Accurately report each monitoring activity.
  •Immediately report critical limit deviations.

## Slide 144: Monitoring examples
Slide 10
Monitoring Example:
  • Time and temperature of process
  • Time and internal temperature combinations
  • Water activity (aw)
  • pH
  • Internal product temperature
  • Salt concentration in brine
  • Metal inclusion screening

## Slide 145: Monitoring equipment examples
Slide 11
Examples of monitoring equipment
  •thermometers
  •recorder charts
  •clocks
  •pH meters
•water activity meters
•data loggers
•metal detectors
•salometer

## Slide 146: Monitoring for XYZ Seafood Company

## Slide 147: End Chapter 8:Principle 4
Monitoring

## Slide 148: Principle 5: Corrective Actions
Slide 1
In this chapter you will learn:
  •The definition of corrective actions,
  •Procedures for corrective actions, and
  •Record-keeping requirements for corrective actions.

## Slide 149: What are Corrective Actions
Slide 2
Slide 3
Definition:
Corrective Action: Procedures to be followed when a deviation occurs.
Predetermined corrective actions are recommended.

## Slide 150: Corrective action components
Slide 4
Corrective action components:
  1)identify the product that was produced during the process deviation, evaluate its safety and determine its disposition.
  2)Correct and eliminate the cause of the deviation and restore process control.
Identify involved product
Assess safety and product disposition
Correct the problem
Restore control

## Slide 151: Is the involved product safe?
Slide 5
Tools to help evaluate product safety:
  •Food Safety Experts
  •Production monitoring data/records
  •NSSP Shellfish Model Ordinance
  •Hazards Guide
    -Appendix 4: Pathogen Tables
    -Appendix 5: Guidance Levels
  •Laboratory testing
Helpful Sources:
FDA Guide-Appendix 4

## Slide 152: Is the involved product safe?
Slide 6
Steps to determine the disposition of the product:
Step 1: Determine if the product presents a safety hazard.
Step 2: If no hazard exists, the product may be released.
Step 3: If a potential hazard exists, determine if the product can be:
  c)Reworked/reprocessed, or
  d)Diverted for a safe use.
Step 4: If a food safety hazard does exist, the product must be rejected or destroyed
Slide 7
Corrective actions must identify the cause of the deviation and restore process control.

## Slide 153: Using the FDA Guide for CA’s
Optional CA’s
In some cases, the final option to reject or destroy product is more logical than trying to produce evidence for other options
FDA Guide Example Chapter 7, page 143

## Slide 154: Information for documenting Corrective Actions
Slide 8
Corrective actions must be documented to indicate the safety status and consequences for the products and process involved.
Page 133

## Slide 155: Example Corrective Actions See pages 134 & 135

## Slide 156: Corrective Actions for XYZ Seafood Company
see page 138-139

## Slide 157: Corrective Actions for XYZ Seafood Company
see page 138-139

## Slide 158: End Chapter 9:Principle 5
Corrective Actions

## Slide 159: Principle 6: Establish Verification Procedure
Slide 1
In this chapter you will learn:
  •The definition of verification
  •Validation is part of verification
  •Verification procedures

## Slide 160: What is Verifications
Slide 2
Slide 3
Definition:
Verification: Those activities, other than monitoring, that determine the validity of the HACCP plan and that verify the system is operating according to the plan.
“Trust what you can verify.”

## Slide 161: Various Types of Verifications
Slide 4
Types of Verification Procedures:
  1)Validation (before the HACCP plan is implemented)
  2)CCP verification (regularly scheduled activities):
  •Calibration of process-monitoring devices,
  •Record review,
  •Targeted sampling and testing.
3)HACCP system verification (periodic activity):
  •HACCP plan reassessment
  •Microbiological end-product testing and third party audits
  4) Regulatory verification (periodic activity)

## Slide 162: Validation ‘before’ operations
‘Will it work’
Slide5
Definition:
Validation: The element of verification focused on collecting and evaluating scientific and technical information to determine if the HACCP plan, when properly implemented, will effectively control the hazards.

## Slide 163: Before operations…‘Validate the HACCP controls and plan will work’
Slide 6
Validation involves establishing the scientific basis for the HACCP plan.
Strategies that can be used to validate the HACCP plan include:
  • using scientific principles and data,
  • relying on expert opinion, or
  • conducting in-plant observations or tests

## Slide 164: When to Validate
Slide 7
Validation frequency:
Before the HACCP plan is implemented
When factors warrant, such as:
  changes in raw materials and/or suppliers
  changes in product or process
  adverse review findings
  recurring deviations
  new scientific information on hazards or control measures
  on-line observations
  new distribution or consumer handling practices

## Slide 165: Verification ‘during’ operations
Slide 8
Slide 9
CCP verification activities:
Calibration of process-monitoring devices
Calibration record review
Targeted sampling and testing
CCP record review
Accuracy checks and calibrations are performed:
On equipment and instruments used in the HACCP plan
At a frequency that ensures accuracy of measurements
‘Is it working’

## Slide 166: ‘Is it working’ … see page 146

## Slide 167: Record Accuracy and Calibration
Slide 11
Slide 12
Frequency of accuracy checks and calibration can depend on:
  Design of the monitoring device
  Reliability and sensitivity of the device
  The environment or conditions in which the device is used
Accuracy checks and calibration records must:
  Document results of accuracy checks and calibration procedures
  Provide a reference to the standard
  Be reviewed by qualified, trained personnel

## Slide 168: Verify through periodic testing
Slide 13
Periodic verification may also include targeted sampling and
laboratory tests of in-process or finished products.

## Slide 169: Must Review Monitoring and Corrective Action Records
Slide 14
Verification through Record Reviews:
  All monitoring and correction action records
  Records must be reviewed within one week from time they were made by an individual who meets the training requirements of the FDA seafood HACCP regulation.

## Slide 170: Total HACCP Program Verification
Slide 15
Slide 16
System-wide HACCP plan verification reviews include:
  Verifying that the hazard analysis and HACCP plan are still accurate, and
  Reviewing records to determine trends and verify that the plan is being followed.
HACCP system verification or reassessment frequency:
  Annually,
  Occurrence of a system failure or significant change in product or process.
Requires a signature

## Slide 171: Total HACCP Program Verification
Slide 17
Slide 18
Situations that may trigger a HACCP plan reassessment:
  A change in products or the process
  A change in the critical limit at a CCP
  Relocation of your plant
  Installation of a new piece of equipment
  A HACCP system failure
  Adverse findings from a regulatory inspection or third party audit
Other system-wide verification strategies
  Finished product testing for microbiological, chemical or physical hazards
  Third-party audits

## Slide 172: Ultimate Verification
Slide 19
Regulatory agencies conduct inspection to verify that a processor:
  Has developed a HACCP plan that controls all significant food safety hazards;
  Has implemented the HACCP plan and it is consistently being used; and
  Is in compliance with HACCP and other regulations.

## Slide 173: Verification Summary…
Pages 152-153

## Slide 174: Verifications for XYZ Seafood Company
pages
155

## Slide 175: Verifications for XYZ Seafood Company
pages
156

## Slide 176: Verifications for XYZ Seafood Company
pages
157

## Slide 177
End Chapter 10:Principle 6
VERIFICATIONS

## Slide 178: Principle 7: Record Keeping Procedures
Slide 1
In this chapter you will learn:
What records are needed
How to develop appropriate records
How to conduct a record review
How computerized records may be used

## Slide 179: Records Support the HACCP Program
Slide 2
Slide 3
1) The HACCP plan and its supporting documentation
Six types of records are needed in a HACCP system:
  1) The HACCP plan and supporting documentation
  2) CCP Monitoring records
  3) Corrective Action records
  4) Verification records
  5) Sanitation Control records
  6) Importer Verification records
Required Records

## Slide 180: Recommended and Required Records
REQUIRED
HACCP Plan
Hazard Analysis
RECOMMENDED

## Slide 181: Additional Record Support for HACCP
Slide 4
Examples of HACCP Plan Support Documents:
Data from published scientific studies
Data from in-plant studies conducted by processing authorities
Data from equipment manufacturers or other authorities
Data gathered in the Preliminary Steps
Pre-requisite programs including sanitation control procedures
Written hazard analysis worksheets

## Slide 182: Records support the HACCP Program
Slide 5
Slide 6
CCP monitoring records are used to document that food safety
hazards have been controlled at each CCP.
Information required on CCP monitoring records:
  Title of record (e.g. Shellfish Receiving Log)
  Firm name and location
  Product identification (if applicable)
  Date and time of monitoring observation
  Actual measurement or observation taken
  Signature or initials of the person performing the monitoring activity
  Signature of the trained person reviewing the monitoring record and the date of review
Required information on required records

## Slide 183: Example Monitoring Records

## Slide 184: Example Monitoring Records …
Pages 163-165

## Slide 185
Information for CA records
…
Pages 165-166
Slide 11
Slide 12
Slide 11
3) Corrective action records

## Slide 186
Slide 13
Slide 14
4) Verification records
Verification records document the results of
  Accuracy and checks and calibration of process-monitoring instruments
  Record Reviews
  Laboratory test results
  In-plant studies or challenge test
  Audits and inspections

## Slide 187: Additional Record Examples …
Pages 168-171

## Slide 188: Do Not Forget Records for required SCP monitoring
Remember SCP records for the 8 Key Sanitation Conditions
Chapter 2
pages 29-39

## Slide 189
Do Not Forget Employee Training Records in GMP’s 117
Page 173

## Slide 190
Slide 23
Slide 24
Electronic or computerized monitoring records must be equivalent to paper records and and written signature
An effective electronic record-keeping system must:
  Be authentic, accurate and protected;
  Provide accurate and complete copies of records;
  Protect records for later retrieval;
  Limit Access to authorized individuals;
  Provide a secure record audit train ; and
  Be reviewed by HACCP trained individual.
Computer Recordkeeping allowed… IF

## Slide 191: Records for XYZ Seafood Company
See pages 180-181

## Slide 192: Records for XYZ Seafood Company
See pages 180-181

## Slide 193: Records for XYZ Seafood Company
See pages 180-181

## Slide 194: SPECIAL NOTE
The HACCP Plan form can be used in portrait format which can be more convenient
XYZ Seafood Company
Pages 184-187
Blank forms are in Appendix 2
Slide 32

## Slide 195: End Chapter11: Principle 7
Record-Keeping
Are ya done !

## Slide 196: The Seafood HACCP Regulation
Slide 1
In this module, you will learn
  •The requirements of the regulation
  •How to reference the specific requirements

## Slide 197: Copies of the Official Published Regulation 21 CFR Part 123 Seafood HACCP Regulation
SHA Training Manual
Appendix 1 (p. 205)
FDA Guide
Addendum 1
Stay aware for periodic additions and updates
Tip

## Slide 198: Regulation Outlined in Parts
Slide 2
Regulation Format
Subpart A — General provision
  •123.3 Definitions
  •123.5 Current GMPs
  •123.6 HACCP plan
  •123.7 Corrective actions
  •123.8 Verification
  •123.9 Records
  •123.10 Training
  •123.11 Sanitation control procedures
  •123.12 Special requirements for imported products
  Subpart B — Smoked and smoke-flavored fishery products
    •123.15 General
    •123.16 Process control
  Subpart C — Raw molluscan shellfish
    •123.20 General
    •123.28 Source controls

## Slide 199: Key Definition in the Regulation
Slide 3
•certification number
•critical control point
•critical limit
•fish
•fishery product
•hazard
•importer
•molluscan shellfish
•preventive measure instrument
•processing
•processor
•scombroid toxin-forming species
•shall
•shellfish-control authority
•shellstock
•should
•shucked shellfish
•smoked or
smoke-flavored fishery
•process-monitoring products
•tag

## Slide 200: Key Definitions in the Regulation
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 4
Slide 5
Regulatory terms ”shall” and ”should”
Ongoing verification:
  •Review of consumer complaints
  •Calibration of process-monitoring instruments
  •Periodic end-product and in-process testing (processor’s option)

## Slide 201: Who must comply?
Slide 6
Products that are subject to regulation:
  • Importer 123.3 (g)
  • Processor 123.3 (k) — domestic and foreign

## Slide 202: Define Processing
Slide 7
What constitutes processing:
  Processing 123.1(l)

## Slide 203: Regulation does not apply to:
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 8
This Regulation doe not apply to
  The harvest or transport of fish or fishery products
  Practices such as heading, eviscerating or freezing intended solely to prepare a fish for holding on a harvest vessel
  The operation of a retail establishment

## Slide 204: Foundation for the Regulation
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 9
Current Good Manufacturing Practices:
  Regulations found in Title 21, Part 117 of the Code of Federal Regulations
  Proper practices for the safe and sanitary handling of all foods
Copy of the current GMP’s Part 117
Appendix 3, Page 233

## Slide 205: Determine hazards likely to occur…
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 10
Slide 11
Hazard Analysis 123.6(a)
Every processor shall conduct, or have conducted for it, a hazard analysis.
Determining those hazards that are “reasonably likely to occur:” Those “for which a prudent processor would establish controls.”

## Slide 206: Witten HACCP Plans….
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•
Slide 12
HACCP Plan 123.6(b)
Every processor shall have and implement a written HACCP plan whenever a hazard analysis reveals one or more food-safety hazards that are reasonably likely to occur.
The plan shall be specific to:
•Each processing location.
•Each species of fish and type of fishery product

## Slide 207: HACCP plans ‘shall’ contain …
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•
Slide 13
The HACCP plan shall list:
  •the food-safety hazards that are reasonably likely to occur.
  •the CCPs.
  •the critical limits.
  •the monitoring procedures.
  •predetermined corrective action plans.*
  •the verification measures.
  •records that will be maintained

## Slide 208: HACCP plans ‘shall’ be signed and dated …
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•
Slide 14
The HACCP plan shall be signed and dated
  •By the most responsible individual at the processing facility or a higher level official.
  -Signed and dated:
    Upon initial acceptance.
    Upon any modification.*
    At least annually.*
*This is a verification

## Slide 209: Special considerations for seafood canning operations
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•
Slide 15
Processors of acidified or low acid canned foods do not need to include controls for C. botulinum in their HACCP plan.

## Slide 210: Sanitation or HACCP Controls?
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 16
Sanitation controls may be difficult to manage in a HACCP plan.

## Slide 211
Slide 17
It is unlawful to process food under conditions that may render it injurious to health.

## Slide 212: Processors ‘shall’ take ‘corrective actions’
Slide 18
Slide 19
Corrective Action 123.7
Whenever a deviation from a critical limit occurs, a processor shall take corrective action.
Corrective Actions — Two Choices:
  3)Predetermined
  4)Alternate Procedure – outlined in the regulation
  -Segregate and hold product
  -Determine product acceptability
  -Apply corrective action to product and process
  -Reassess the HACCP plan

## Slide 213: Verifications are required…
Every processor shall verify:
•That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
•That the HACCP plan is implemented effectively.
Slide 20
Slide 21
Every processor shall verify:
  •That the HACCP plan is adequate to control the food-safety hazards that are reasonably likely to occur; and
  •That the HACCP plan is implemented effectively.
Ongoing verification:
  •Review of consumer complaints
  •Calibration of process-monitoring instruments
  •Periodic end-product and in-process testing (processor’s option)

## Slide 214: Information required on each record …
Slide 23
Required information on each record:
  •Name and location of the processor or importer
  •Date and time of the activity being recorded
  •Signature or initials of the person making the record
  •Identity of the product and the production code where appropriate

## Slide 215: Required record…
Slide 23
Records required by the regulation:
  •HACCP plan(s)
  •Monitoring records
  •Corrective action records
  •Verification records
  •Sanitation control records
  •Importer verification records

## Slide 216: Record Reviews and Retention …
Slide 24
Slide 25
Review of records:
  •CCP monitoring and corrective action records – within one week
  •Calibration and in-process or end-product testing records –timely manner
Record Retention
  •One year for refrigerated products
  •Two years for frozen or preserved products

## Slide 217: HACCP training to …
Slide 26
The HACCP-trained individual shall:
  •Develop the HACCP plan.
  •Reassess and modify the HACCP plan and hazard analysis.
  •Review HACCP records.
Trained

## Slide 218: SCP’s – Sanitation Control Procedures
Slide 27
  • Processors should have written SCPs.
  •Processor shall monitor and document sanitation control procedures.
  •Processors shall correct sanitation deficiencies in a timely manner.

## Slide 219: 8 Key Sanitation Control Areas
Slide 28
Eight key sanitation areas:
1)Safety of water,
2)Condition and cleanliness of food-contact surfaces,
3)Prevention of cross-contamination,
4)Maintenance of hand-washing, hand-sanitizing and toilet facilities,
5)Protection from adulterants,
6)Labeling, storage and use of toxic compounds,
7)Employee health conditions,
8)Exclusion of pests.

## Slide 220: HACCP with Imported Seafood
Slide 30
Slide 29
Importer Verification:
Importer Verification Procedures
Importers must have:
•Import from countries with a memorandum of understanding (MOU) or
•Implement verification procedures.
1)Written verification procedures
2)Product specifications
3)Affirmative steps

## Slide 221: HACCP with Imported Seafood
Slide 31
Affirmative steps may include any of the following:
  •Obtain foreign processor’s HACCP and sanitation monitoring records for the lot being entered
  •Obtain continuing or lot-by-lot certificate from competent third party
  •Regularly inspect foreign processor
  •Obtain foreign processor’s HACCP plan and written guarantee that regulation is being met
  •Test the product and obtain written guarantee that regulation is being met
  •Perform other verification procedures that provide the equivalent level of assurance

## Slide 222: HACCP with Smoked Seafood
Slide 32
Smoked and Smoke-Flavored Fishery Products
  •HACCP plan must include controls for Clostridium botulinum toxin formation for the shelf life of the product under normal and moderate abuse conditions.
  • Where product is subject to 21 CFR 113 or 114, the HACCP plan need not include such controls.

## Slide 223: HACCP with Imported Seafood
Slide 32
Smoked and Smoke-Flavored Fishery Products
  •HACCP plan must include controls for Clostridium botulinum toxin formation for the shelf life of the product under normal and moderate abuse conditions.
  • Where product is subject to 21 CFR 113 or 114, the HACCP plan need not include such controls.

## Slide 224: HACCP with Raw Molluscan Shellfish
Slide 33
Raw Molluscan Shellfish 123.20
  •HACCP plans must include a means for controlling the origin of the raw molluscan shellfish.
  •Where processing includes a treatment that ensures the destruction of vegetative cells of microorganisms of public health concern, the HACCP plan need not include controls on sources of origin.

## Slide 225: HACCP with Raw Molluscan Shellfish
Slide 34
Slide 35
Raw Molluscan Shellfish 123.28
Shellstock Receiving:
  •If source is a harvester, harvester must be in compliance with any license requirement.
  •If source is another processor, processor must be certified by a shellfish-control authority.
  •Containers of shellstock must be properly tagged.
Raw Molluscan Shellfish 123.28
Processors shall only process molluscan shellfish from:
  •Growing waters approved by a shellfish-control authority
  •Federal growing waters not closed by an agency of the federal government

## Slide 226
Slide 36
Slide 37
Raw Molluscan Shellfish 1240.60 (b)
Required information on tag:
  •Date and place shellfish were harvested (state and site)
  •Type and quantity of shellfish
  •Harvester identification number, name of harvester or name or registration number of harvester’s vessel
Raw Molluscan Shellfish 123.28
Records for shellstock receiving must document:
Date of harvest
  •Location of harvest by state and site
  •Quantity and type of shellfish
  •Date of receipt by the processor
  •Name of harvester, name or registration number of the harvester’s vessel or harvester’s identification number

## Slide 227
Slide 38
Slide 39
Raw Molluscan Shellfish 123.28
Shucked molluscan shellfish containers must bear a label that contains:
  •Name of packer or repacker
  •Address of packer or repacker
  •Certification number of packer or repacker
Raw Molluscan Shellfish 1240.60 (c)
Records for shucked product must document:
•Date of receipt
•Quantity and type of shellfish
•Name and certification number of the packer or repacker

## Slide 228: Resources for Preparing Seafood HACCP Plans
Resources are available through FL Sea Grant Website:
https://www.flseagrant.org/wp-content/uploads/2024/10/Seafood-and-HACCP-Resources-For-Insturctors_Updated-9-2024-2.pdf

## Slide 229: Course Closeout
Certificates are sent via email within two weeks of AFDO receiving course closeout paperwork.
Make sure you can receive emails from haccp@afdo.org.
If certificate is not received, first check your junk folder, then contact your instructor.
Confirm certificate information is accurate upon receipt.
NOTE: there is a $15 fee to have certificates re-issued or revised more than 3 months after it was issued.

## Slide 230
Contact Dr. Razieh Farzad with any questions or comments about these slides.
Email:rfarzad@ufl.edu
Phone number: (352)-2945-3902